## Slide 1: Temperature & Humidity Measurement
Embedded Linux
By: John Padoginog, Steven Selementi, David Bisgrove

## Slide 2: Project Description
Collects temperature & humidity.
  Records at user-inputted intervals.
Stores data locally and remotely.
External website displays recorded data.
  Requires user login.
  Ability for frequency and timeframe adjustment.

## Slide 3: Goals
Successful reading of temperature and humidity via DHT22 sensor.
  Data table with recordings.
Administrative website:
  Displays data.
  Set frequency and time frame.
Acquire skills in:
  Python programming.
  Web programming/design.
  Team skills.

## Slide 4: Implementation
Our project implementation was broken into two major parts:
Operating Python code (Raspberry Pi):
  Reads and stores temperature and humidity values.
  Variable timeframe and frequency parameters.
  Stores values into an SQL database.
Online Website (Wyvern):
  Displays data tables remotely.
  HTML Based.
  Control of timeframe and frequency remotely.

## Slide 5: Physical Components
Raspberry Pi 3
Adafruit DHT22 Sensor
Breadboard
4.7K Resistor
Jumper wires
T-Cobbler

## Slide 6: Software
Python
SQLite3
PHP
Wyvern
FileZilla

## Slide 7: Process
Our system is set up to have communication between our local (Pi) and remote component (Webserver).
Raspberry Pi:
  Powered with 5V power adapter
  Connected to breadboard via T-Cobbler Plus
  DHT22 Sensor:
    1: VCC(3.3V)
    2: Data – Connected to GPIO pin 04
    3: N/A
    4: GND
  Python Code:
    Reads and stores data into SQL database.
    Set up to communicate to Wyvern Webserver.
    Variable frequency and timeframe.

## Slide 8: Process (cont.)
Remote webserver:
  PHPMyAdmin
  Apache2

## Slide 9: Aspects
The Good:
  Operating temperature and sensor reading
  User input for variable frequency and timeframe
  New knowledge of:
    Python
    Webserver Configuration
The Bad:
  Invalid permissions for PHPMYADMIN

## Slide 10: References
http://www.instructables.com/id/Turning-your-Raspberry-Pi-into-a-personal-web-serv/
http://www.instructables.com/id/Raspberry-PI-and-DHT22-temperature-and-humidity-lo